## Slide 1: Worker Protection Standard Pesticide Emphasis
Presented by Oregon OSHA Public Education

## Slide 2: Oregon OSHA Public Education Mission:
We provide knowledge and tools to advance self-sufficiency
in workplace safety and health.
Oregon OSHA Services
Consultation Services
Enforcement
Appeals
Public Education and Conferences
Standards and Technical Resources

## Slide 3: Contact us
Field Offices:
Portland 503-229-6193
Salem 503-373-7819
Eugene 541-686-7913
Medford 541-776-6016
Bend 541-388-6068
Pendleton 541-276-2353
Salem Central
Toll Free English:
800-922-2689
Toll Free Spanish:
800-843-8086
Website: osha.oregon.gov

## Slide 4: Goals
Identify the requirements of the WPS.
Differentiate between Oregon OSHA and WPS rules.
Identify the components of an effective WPS program.
Identify the eight label elements of the WPS.

## Slide 5: Introduction
Environmental Protection Agency (EPA)’s Pesticide Worker Protection Standard (WPS)
Oregon OSHA enforces…

## Slide 6: Heat and wildfire smoke Permanent rules effective in Oregon beginning in 2022
Heat
Heat Index
Shade
Water
Rest break
Acclimatization
Prevention plan
Wildfire Smoke
Exposure
AQI
Respirators
Exposure monitoring and training
Communication
Engineering and administrative controls

## Slide 7: When Worker Protection applies to you
Pesticides have been applied or a restricted entry interval (REI) has been in effect within the last 30 days at your establishment.
The pesticide applied has an “Agriculture Use Requirements” Box on the label.
You employ pesticide handlers, and/or hand-labor workers on an agricultural, forest, or nursery operation. This includes outdoor and indoor spaces.

## Slide 8: When Worker Protection does NOT apply to you
Pest control
Livestock
Non-commercial/Research
Gardens, parks, golf courses
Direct injection
Non-crop areas
Attractants/Repellents
Harvested portions

## Slide 9: Definitions
Workers
Handlers

## Slide 10: Required postings and record retention
Display or make available all information in an easily accessible (central) location on the agricultural establishment.

## Slide 11: Protection for both workers and handlers – a Q&A Pesticide Safety Training
When must workers and handlers be trained?
How often must workers and handlers be trained?
How do I train my workers and handlers?
Who can provide the training?
What about employees who speak a different language?
How long do I need to keep the training documentation?
Where should I train my employees?

## Slide 12: Training records
Worker’s or handler’s printed name and signature
Date of training
Trainer’s name
Trainer’s qualifications
Employer’s name
Identification of EPA approved training materials

## Slide 13: Sources
Environmental Protection Agency (EPA):
  Phone: 1-888-663-2155
  Website: www.epa.gov
Pesticide Educational Resources Collaborative:
  Website: www.pesticideresources.org

## Slide 14: Training Exercise (page 16) For English language learners in the group
Language Leader:
Bilingual person with good speaking skills.
Social Leader:
A person who is viewed as a leader by the group.
Technical Leader:
The person with the best job and safety-related knowledge (usually the most experienced).

## Slide 15: Decontamination supplies
1 Gallon of Water : Person
3 Gallons of Water : Handler
Eye Wash : “Danger” or
“Danger Poison” Label

## Slide 16: Handler
Location and description
Date, start, and end time
Product name, EPA registration (#), active ingredients, REI
Oral warnings, and treated area posting
Other safety requirements

## Slide 17: Employer
Specific location and description of any treated areas at their workplace where an REI is in effect that the commercial handler may be in or walk within 1/4 mile
Restrictions on entering those areas

## Slide 18: Exposed to pesticides
Transportation to emergency treatment
Provide information related to the pesticide to emergency personnel

## Slide 19: Reporting requirements for ALL employers
Within 8 hours:
All work-related fatalities and catastrophes
Within 24 hours:
Any work-related:
Inpatient hospitalization
Amputation or avulsion
Loss of an eye
To report an incident, call Oregon OSHA’s toll-free line 24 hours a day, 7 days a week at 1-800-922-2689, or call your nearest Oregon OSHA field office. If a workplace death occurs on a holiday, or during the weekend, do not wait until regular business hours to report the workplace death.

## Slide 20: Agricultural employers: Restrictions during application
The application exclusion zone (AEZ) for outdoor production.
A specific area that varies by the type of application until the ventilation criteria are met for enclosed space production.

## Slide 21: Restricted Entry Intervals (REIs)
If the pesticide label has notification directions, you must follow them.
If there are no notification directions on the label, you must either verbally warn or post signs.
If the REI is greater than 48 hours for an outdoor application, you must post signs.
If the REI is greater than 4 hours for an enclosed space (greenhouse) application, you must post signs.
Tell workers which method is in effect.

## Slide 22: Levels of respiratory protection
Review the chart on page 23. It lists images and descriptions of the most protective to least protective NIOSH respirators.

## Slide 23: What is the Application Exclusion Zone (AEZ)?
AEZ YouTube Videos
English
Spanish

## Slide 24: Posting information
Agricultural employer requirements:
ALH only
Information station
How to prevent or reduce pesticide exposure
Location of pesticide safety information
pesticideresources.org/wps/cp.html

## Slide 25: Exercise (page 28)
What are the AEZ Requirements?
Review the decision matrix on page 27 for the Worker Protection Standard, Application Exclusion Zone.
Complete the scenarios on page 28.

## Slide 26: Application notification
Additional protection for workers
What do I need to do to notify my workers about a pesticide application?
What does a verbal warning mean?
What about warning the public about restricted entry?

## Slide 27: Application notification
Additional protection for handlers
Application restrictions and monitoring
  Specific instructions for handlers
Equipment
  Equipment safety for handlers
  Personal protective equipment
Remember to take steps to avoid heat-related illness when labeling requires the use of PPE for a handler activity.

## Slide 28: WPS glove requirements
Pilots
Handlers and early entry workers
Glove liners
Hot or cold periods

## Slide 29: Care of PPE
Store
Wash
Respirators
Disposal
Instructions for people who clean PPE

## Slide 30: Not directly employed by the establishment
Provide the following information:
The equipment may be contaminated with pesticides.
The potentially harmful effects of pesticide exposure.
How to handle equipment to limit exposure to pesticides.
How to wash themselves and/or their clothes to remove and prevent exposure to pesticide residues. Reference ORS 170.309 and 170.313(1).

## Slide 31: Eight items to notice on labels
Application restriction statement
40 CFR part 170 reference statement
Product-type identification statement
State restrictions
Spanish warning statement
Restricted entry statement
Notification-to-workers statement
Personal protective equipment statement

## Slide 32: Review (page 36)
Parts of the label

## Slide 33: Review - which rule applies Have pesticides been applied, or has a restricted-entry interval been in effect within the last 30 days?

## Slide 34: Last 30 days
Location of application
Product name
EPA registration (#)
Active ingredients
Time and date of the application
Restricted entry interval
Area treated | Product name | EPA Reg. number | Common name Active ingredient | Application Month/Day/ Time | Restricted entry interval | Do not enter until: Month/Day/Time
Example pesticide application record on next slide.

## Slide 35: Example pesticide application record
Area treated | Product name | EPA Reg. number | Common name Active ingredient | Application Month/Day/ Time | Restricted entry interval | Do not enter until: Month/Day/Time
Pears Home Place | Dimethoate 2.67EC | 34704-489 | Dimethoate | May 5th - 11 a.m. | 10 days | May 15th - 11 a.m.
Blueberries Abilene Block | Captan 4L | 19713-644 | Captan | April 11th - 10:30 a.m. | 48 hours | April 13th- 10:30 a.m.
Grass Seed Field/Howell Prairie | Roundup Ultra | 524-475 | Glyphosate | March 25th - 2 p.m. | 4 hours | March 25th - 6 p.m.

## Slide 36: Additional Educational Resources
Oregon OSHA’s YouTube Channel
A-Z Topic Index
Oregon OSHA Online Training Courses
PESO – English to Español
Other Safety and Health Training Resources

## Slide 37: Need more information? Call your nearest Oregon OSHA Office
Salem Central Office
350 Winter St. NE
Salem, OR 97301-3882
Phone: 503-378-3272
Toll-Free: 800-922-2689
Fax: 503-947-7461
en Español: 800-843-8086
Website: osha.oregon.gov
Bend
Red Oaks Square
1230 NE Third St., Suite A-115
Bend, OR 97701-4374
541-388-6066
Consultation: 541-388-6068
Eugene
1500 Valley River Drive, Suite 150
Eugene, OR 97401-4643
541-686-7562
Consultation: 541-686-7913
Medford
1840 Barnett Road, Suite D
Medford, OR 97504-8293
541-776-6030
Consultation: 541-776-6016
Pendleton
750 SE Emigrant Ave., Suite 131
Pendleton, OR 97801
541-276-9175
Consultation: 541-276-2353
Portland
Durham Plaza
16760 SW Upper Boones
Ferry Road, Suite 200
Tigard, OR 97224-7696
503-229-5910
Consultation: 503-229-6193
Salem
1340 Tandem Ave. NE, Suite 160
Salem, OR 97301-8080
503-378-3274
Consultation: 503-373-7819

## Slide 38: Thank you!